## Slide 1: theoretical Aspects of patch clamping: Session 1
William A. Coetzee NYU School of Medicine

## Slide 2: Contents
Basic bioelectricity
The operational amplifier
A simple voltage-clamp circuit

## Slide 3: Electricity 101
The capacitor
  Two plates separated from each other by a space that is filled with a non-conducting substance called a dielectric
  Charge separation
    q = C.V
    C is measured in farads (F) and is a physical characteristic of a capacitor

## Slide 4
Prefix | Symbol | Multiplication | 
giga | G | 1,000,000,000 | 109
mega | M | 1,000,000 | 106
kilo | k | 1,000 | 103
milli | m | 0.001 | 10-3
micro | m | 0.000,001 | 10-6
nano | n | 0.000,000,001 | 10-9
pico | p | 0.000,000,000,001 | 10-12
femto | f | 0.000,000,000,000,001 | 10-15
atto | a | 0.000,000,000,000,000,001 | 10-18

## Slide 5: The cell membrane is a capacitor
-
-
-
-
+
+
+
+
+
+
+
+
-
-
-
-
+
-
+
q = Cm.Vm
IC = dq/dt = Cm.(dVm/dt)
IC

## Slide 6: Battery

## Slide 7: The membrane is a battery
+
+
+
+
-
-
-
-
-80mV

## Slide 8: The resistor
A circuit element that opposes the movement of charge
Ohm’s law
  I = V/R
Conductance is the inverse of resistance
  g = 1/R
Units
  Resistance: Ohms (Ω)
  Conductance: Siemens (S)

## Slide 9: The membrane is a resistor
-
-
-
-
+
+
+
+
+
-
I = Vm/Rm
Or
I = Vm* gm

## Slide 10: The membrane is a resistor and a capacitor in parallel
-
-
-
-
+
+
+
+
+
-
Im = IR + IC
Im = Vm/Rm + Cm.dVm/dt
+
+
+
+
-
-
-
-
-
-
-
-
+
+
+
+
+
Im

## Slide 11: The Current-Voltage Relationship
Voltage (V or E)
 Outward
Current (I)
Inward 
G=I/V
+
+
+
+
-
-
-
-
-
-
-
-
+
+
+
+
+

## Slide 12: Equivalent Circuit of the Cell Membrane
The capacitive property of the phospholipid backbone of the membrane is modeled as a capacitor, a water-filled pore in the membrane is modeled as a resistor, and the equilibrium potential for an ion is modeled as a battery in series with the membrane channel

## Slide 13: The Current-Voltage Relationship
Voltage (V or E)
Current (I)
G=I/V
Erev

## Slide 14: A Diode (rectifier)
Rectification
  Outward
  Inward
I
V
Outward
Inward

## Slide 15: Contents
Basic bioelectricity
The operational amplifier
A simple voltage-clamp circuit

## Slide 16: The Operational Amplifier
+
-
+V
-V

## Slide 17: Patch clamping
Allows the measurement of ion channel activity in cells or membrane patches
Voltage clamping vs current clamping
Erwin Neher and Bert Sakmann (early 80‘s)
  Nobel Prize in Physiology or Medicine in 1991

## Slide 18: Patch clamping

## Slide 20: Patch clamp configurations
Cell-attached (on-cell)
  Loose patch
Whole-cell
  Perforated patch
Inside-out
Outside-out

## Slide 21: Operation of the operational amplifier
The rules:
  The output attempt to do whatever it takes to make the voltage difference between the input terminals zero
  The input terminals draw almost no current (i.e. the input impedance is extremely high)
  The output impedance is very low
+
-
+V
-V

## Slide 22: A Voltage Divider
Vout
Vin
R1
R2

## Slide 23
Rpip = 2 MΩ
Rin = 20MΩ
Vm = -80mV
I

## Slide 24
Rpip = 2 MΩ
Rin = 1012Ω
Vm = -80mV

## Slide 25: Inverting Amplifier
+
-
R1
R2
Vin
Vout
I1
I2
Kirchhoff's first law, or Kirchhoff's current law (1854)
At any point in an electrical circuit, the sum of currents flowing towards that point is equal to the sum of currents flowing away from that point
Gain function: -R2/R1

## Slide 26: Summing inverted amplifier with offset
+
-
R1
R1
V2
Vout = -(V1+V2) + Vx
R1
V1
+
-
Vx

## Slide 27
+
-
R1
R2
Vin
Vout
I1
I2
V-
V- = Vin
Gain function: 1+(R2/R1)
Non-inverting amplifier

## Slide 28: Differentiator
+
-
C
R
Vin
Vout
I1
I2

## Slide 29: Integrator
+
-
C
R
Vin
Vout
I1
I2

## Slide 30: The Bode Plot
Graph of the magnitude of the gain in decibels (dB) as a function of the frequency of the input signal
The gain expressed in decibels (dB)
20 log10(Vout/Vin)

## Slide 31: Frequency response of an operational amplifier
-3dB point:
The bandwidth is the frequency at which the power of the output signal is reduced to half that of the maximum
-6dB/octave

## Slide 32: Phase-lag relationship

## Slide 33: Contents
Basic bioelectricity
The operational amplifier
A simple voltage-clamp circuit

## Slide 34
Em
Command potential
Current
Two-electrode voltage clamping